## Slide 1
Tc Calculator and VCRat 2.6 Training Class
VCWPD December 2008
Tom Lagier, Director
Sergio Vargas, Deputy Director
Hydrology Section
Mark Bandurraga
Scott Holder

## Slide 2: Tc Calculator
Automates Tc Calculation
Includes J, J’, K, and L Zone Rainfall
10-, 25-, 50-, and 100-yr frequencies
Consistent with 1991 Manual methodology
Increases the number of required calculations for hydrology models

## Slide 3: Website Products
Intranet- http://watershedweb/hydrology/
Tc Calculator bundled with VCRat 2.6
Tc Calculator Manual
2006 Hydrology Manual
Training Materials

## Slide 4: Tc Calculator Resources
Tc Calculator Program and Manual
1/07 and 12/08 Training Materials
2006 Hydrology Manual
  Description of method
  Exhibits for Hand Calculation
  Blank Hand Calculation Form
  Three examples with Calculator Output
  GIS Files for Workmap creation

## Slide 5: Tc Calculations
Sub-area delineation (40-80 ac rec)
Define sub-area flow-paths (overland, natural or valley channel, street, pipe, channel) and delineate areas.
Calculate flow-path areas and percents, lengths, elevations, slopes
Define soil, rain zone, storm

## Slide 6: Overland Flow Areas
Undeveloped area max length 1,000 ft or to point where contours indicate channel
Developed area max length 200 ft
If undeveloped, check for scour velocity
100- and 50-yr min velocity=1.0 fps (If very low slope, min=0.5 fps but do by hand)
25- and 10-yr min velocity=0.5 fps

## Slide 7: Other Topics
Provides peak flow for single subarea
Overland flow slope limited to 0.35 ft/ft- higher slopes will be reduced to 0.35 ft/ft
Use of tab might mess up data
Sensitive to data input- highlight and overwrite

## Slide 8: New Features in TC Calc 2.6
Corrected memory issues that crashed program when deleting subareas.
Can move subareas up or down in tree to change the order.
New summary report.
Enhanced scour error check.
Fixed several bugs.

## Slide 9: Tc Demonstrations
Brown Barranca Subarea 1A Undeveloped
Brown Barranca Subarea 29B Residential
Training Exercise 1- Use Tc Calculator to calculate Tc for Brown Barranca Subarea 2A- Undeveloped

## Slide 10
VCRat 2.6 Training Class
December 8, 2008
Ventura County Government Center
Mark Bandurraga
Scott Holder
“DOS!! What’s DOS?”
“Don’t you guys have a Windows version of VCRat?”
“There must be an easier way than entering data in a text file?”
“Why doesn’t this model run? Why is it stuck in an error loop?”
“I need a ‘1’ in what column?”
“HELP!!!!!!”
“What is a 005 Card?”

## Slide 11: Introducing VCRat 2.6
The new update Windows-friendly version of VCRat.

## Slide 12: What are We Covering?
VCRat Methodology
VCRat 2.6 Complexities
Getting Started / Getting Help
Running/Importing an existing VCRat 2.2 Model
Starting a Model from Scratch
Adding Model Points
Channel Routing
Areal Reduction/ Fattening / Yield Adjustment
Questions

## Slide 13: VCRat Methodology
Modified Rational Method- Uses rainfall hyetograph to simulate a hydrograph that can be confluenced with other subareas.
Includes Channel and Reservoir Routing (Modified Puls)
Program intended to model watersheds - not for catch basins or 1-ac subareas lots. (i.e 40-80 acres recommended)

## Slide 14: What is VCRat 2.6?
Still uses the core VCRat 2.2 Fortran Program (with a few modifications).
Provides a Windows interface to enter and run a model.
File structure is now Windows compliant. Also has been tested
with Windows Vista.
Integrated help system.
New model output report.
Better parameter checking.
Now can use both J and J’
curves at the same time

## Slide 15: VCRat 2.6 Complexities
No Recycling capability for Areal Reduction.
Imported VCRat 2.2 models may not run or yield same answers.
Only performs the 4th day storm.
Identifies change in channel type with # sign if program is auto-selecting channels
For routed Q value need placeholder line
No extrapolation of basin stage-storage curve
VCRAIN.DAT file same as required for Tc Calculator; different format than used in VCRat 2.2

## Slide 16: Getting Started / Getting Help
Install package places a shortcut on desktop.
VCRat and TcCalc are found under the Start Menu. Start -> VCWPD Hydrology -> VCRat 26.
Help menu on Main Window.
The ‘?’ on dialogue boxes.
Searchable help file.
Hydrology Manual and help files also available from Start Menu.

## Slide 17: Importing an Existing VCRat 2.2 Model
Use Import VCRat2… under the File menu.
Select the VCRat 2.2 File.
Any issues or warnings will be displayed and can be saved.
Save the model in .vin format
and correct any issues/warnings
if desired.

## Slide 18: Running a Model
Use Run Model under the Model
menu.
Any issues or warnings will be displayed and can be saved.
Model DOS Window will appear.
Model output file will appear after
successful run.
If stuck in endless loop, use task
manager to stop

## Slide 19: New Features in VCRat 2.6
Usability features such as double-click opens edit window, and remembers last selected operation.
Models can use relative paths instead of the absolute paths in VCRat 2.5.
Import and Export hydrographs and stage-storage-discharge curves to comma separated (csv) files.
Add or Insert a copy of another operation.
Reservoir routing can be turned off for a run without deleting reservoir info.
Hydrographs outputs are now to 2 decimal places so volumes can be calculated correctly.
Fixed several know bugs and enhanced the error catching routines.
Make VCRat 2.6 run on Windows Vista. (Has been tried on one computer but unknown if it runs on all configurations of Windows Vista).

## Slide 20: VCRat 2.6 Demonstration
Importing/Running VCRat 2.2 Model
Starting a Model from Scratch
Adding Model Points
Adding Stream Routing
Adding Reservoir / Fattening
Viewing and Exporting Hydrographs

## Slide 21: Questions?